## Slide 1: Steam Tables Tutorial (Illustration of Steam Tables Process Overview)
Fundamentals of Engineering Thermodynamics
8th Edition
by Moran, Shapiro, Boettner, and Bailey,
2014

## Slide 2
Given: p1 = 30 bar, T1 = 320oC
T
v
p1 = 30 bar
Tsat1 = 233.9oC
•
1
T1 = 320oC
From Table A-3 @ p1 = 30 bar
Tsat1 = 233.9oC
Conclusion: Since T1 > Tsat1,
State 1 is Superheated vapor
Obtain properties from Table A-4
Superheated
vapor
Example 1 (p and T given)

## Slide 3
1
Given: p1 = 30 bar, T1 = 320oC
From Table A-2 @ T1 = 320oC
psat1 = 112.7 bar
Conclusion: Since p1 < psat1,
State 1 is Superheated vapor
Obtain properties from Table A-4
Example 1 (p and T given)
p
v
T1 = 320oC
psat1 = 112.7 bar
•
p1 = 30 bar
Superheated
Vapor

## Slide 4
Given: p2 = 25 bar, T2 = 100oC
T
v
p2 = 25 bar
Tsat2 = 224.0oC
•
T2 = 100oC
From Table A-3 @ p2 = 25 bar
Tsat2 = 224.0oC
Conclusion: Since T2 < Tsat2,
State 2 is Compressed liquid
Obtain properties from Table A-5 or A-2 (approximate as saturated liquid)
Compressed
liquid
Example 2 (p and T given)
2

## Slide 5
Given: p2 = 25 bar, T2 = 100oC
From Table A-2 @ T2 = 100oC
psat2 = 1.014 bar
Conclusion: Since p2 > psat2,
State 2 is Compressed liquid
Obtain properties from Table A-5 or Table A-2 (approximate as saturated liquid)
Example 2 (p and T given)
p
v
T2 = 100oC
psat2 = 1.014 bar
p2 = 25 bar
Compressed
liquid
•
2

## Slide 6
Two-phase
liquid-vapor
mixture
Given: p3 = 5 bar, T3 = 151.9oC
T
v
p3 = 5 bar
Tsat3 = T3 = 151.9oC
3?
T3 = 151.9oC
From Table A-3 @ p3 = 5 bar
Tsat3 = 151.9oC
Conclusion: Since T3 = Tsat3,
State 3 is Two-phase liquid-vapor mixture
Need another property to obtain properties
Example 3 (p and T given)

## Slide 7
Given: p4 = 15.54 bar, T4 = 200oC
From Table A-2 @ T4 = 200oC
psat4 = 15.54 bar
Conclusion: Since p4 = psat4,
State 4 is Two-phase liquid-vapor mixture
Need another property to obtain properties
Example 4 (p and T given)
p
v
T4 = 200oC
psat4 = p4 = 15.54 bar
p4 = 15.54 bar
Two-phase
liquid-vapor
mixture
4?

## Slide 8
Given: T5 = 80oC and v5 = 0.0010200 m3/kg
From Table A-2 @ T5 = 80oC
vf5 = 0.0010291 m3/kg and vg5 = 3.407 m3/kg
Conclusion: Since v5 < vf5,
State 5 is Compressed liquid
Obtain properties from Table A-5 or Table A-2 (approximate as saturated liquid)
Example 5 (T and v given)
v5 = 0.0010200
Compressed
liquid
T
v (m3/kg)
T5 = 80oC
vg5 = 3.407
•
vf5 = 0.0010291
5

## Slide 9
Given: T6 = 80oC and v6 = 1.2 m3/kg
From Table A-2 @ T6 = 80oC
vf6 = 0.0010291 m3/kg and vg6 = 3.407 m3/kg
Conclusion: Since vf6 < v6 < vg6,
State 6 is Two-phase liquid-vapor mixture
Determine quality (x6) and use quality calculations to compute desired properties
Example 6 (T and v given)
v6 = 1.2
Two-phase
liquid-vapor
mixture
T
v (m3/kg)
T6 = 80oC
vg6 = 3.407
•
vf6 = 0.0010291
6

## Slide 10
Given: T7 = 80oC and v7 = 4.625 m3/kg
From Table A-2 @ T7 = 80oC
vf7 = 0.0010291 m3/kg and vg7 = 3.407 m3/kg
Conclusion: Since v7 > vg7,
State 7 is Superheated vapor
Obtain properties from Table A-4
Example 7 (T and v given)
v7 = 4.625
Superheated
vapor
T
v (m3/kg)
T7 = 80oC
vg7 = 3.407
•
vf7 = 0.0010291
7

## Slide 11
Given: p8 = 80 bar and u8 = 1200 m3/kg
From Table A-3 @ p8 = 80 bar
uf8 = 1308.6 kJ/kg and ug8 = 2569.8 kJ/kg
Conclusion: Since u8 < uf8,
State 8 is Compressed liquid
Obtain properties from Table A-5 or Table A-2 (approximate as saturated liquid)
Example 8 (p and u given)
u8 = 1200
Compressed
liquid
p
u (kJ/kg)
p8 = 80oC
ug8 = 2569.8
•
uf8 = 1308.6
8

## Slide 12
Given: p9 = 80 bar and u9 = 1600 kJ/kg
From Table A-3 @ p9 = 80 bar
uf9 = 1308.6 kJ/kg and ug9 = 2569.8 kJ/kg
Conclusion: Since uf9 < u9 < ug9,
State 9 is Two-phase liquid-vapor mixture
Determine quality (x9) and use quality calculations to compute desired properties
Example 9 (p and u given)
u9 = 1600
Two-phase
liquid-vapor
mixture
p
u (kJ/kg)
p9 = 80 bar
ug9= 2569.8
•
uf9 = 1308.6
9

## Slide 13
Given: p10 = 80 bar and u10 = 3102.7 kJ/kg
From Table A-3 @ p10 = 80 bar
uf10 = 1308.6 kJ/kg and ug10 = 2569.8 kJ/kg
Conclusion: Since u10 > ug10,
State 10 is Superheated vapor
Obtain properties from Table A-4
Example 10 (p and u given)
u10 = 3102.7
Superheated
vapor
p
u (kJ/kg)
p10 = 80 bar
ug10 = 2569.8
•
uf10 = 1308.6
10

## Slide 14
Given: T11 = 80oC and x11 = 0.6
Conclusion:
State 11 is Two-phase liquid-vapor mixture
Use quality calculations with saturated liquid (f) and saturated vapor (g) values from Table A-2 to compute desired properties
Example 11 (T and x given)
v11 = 2.045
Two-phase
liquid-vapor
mixture
T
v (m3/kg)
T11 = 80oC
vg11 = 3.407
•
vf11 = 0.0010291
11
x11 = 0.6
From Table A-2 @ T11 = 80oC
vf11 = 0.0010291 m3/kg and vg11 = 3.407 m3/kg

## Slide 15
Given: p12 = 80 bar and x12 = 0.6
Conclusion:
State 12 is Two-phase liquid-vapor mixture
Use quality calculations with saturated liquid (f) and saturated vapor (g) values from Table A-3 to compute desired properties
Example 12 (p and x given)
u12 = 2065.3
Two-phase
liquid-vapor
mixture
p
u (kJ/kg)
p12 = 80 bar
ug12 = 2569.8
•
uf12 = 1308.6
12
x12 = 0.6
From Table A-3 @ p12 = 80 bar
uf12 = 1308.6 kJ/kg and ug12 = 2569.8 kJ/kg